## Slide 1
UrjaSetu
Microgrid Energy Mix Optimizer:
Automatic dispatch that makes operators trust the system
Deciding, every fifteen minutes, exactly how to blend solar, wind, battery, and diesel — so the lights never depend on guesswork.
Solar
Wind
Battery
Diesel
Team TATVA
HackOut'26 · Renewable Energy Intelligence
Notes: Picture a village where the lights cut out right as someone's finishing dinner on an induction stove. Not because there's no power on site — there's solar on the roofs, a battery bank, a diesel genset sitting there as backup. The power just... didn't get to the right place at the right time. That's the problem we picked. We're Team Tatva, and we built a system that decides, every fifteen minutes, exactly how to blend solar, wind, battery, and diesel so that doesn't happen. This is our build for HackOut'26, Renewable Energy Intelligence.

## Slide 2
01 · PROBLEM STATEMENT
Inefficient Dispatch Decisions Increase Operating Costs
Right now dispatch is either a fixed schedule — diesel runs six to nine, no matter what — or whatever the operator on duty feels like doing. That produces three costly patterns, over and over:
Diesel burns needlessly
Generator kicks in even when solar was already covering the load.
Batteries die early
Poor cycling and deep discharges wear packs out years ahead of schedule.
Blackouts catch everyone off guard
No one is watching the shortfall coming until it's already dark.
TATVA · UrjaSetu · HackOut'26
02 / 16
Notes: Here's the thing nobody tells you about off-grid microgrids: the hardware's basically solved. Panels are cheap, batteries are cheap, gensets are everywhere. What's missing is the decision-making. Right now it's either "diesel runs six to nine, no matter what," or it's whatever the operator on duty feels like doing that day. And that gets you three bad outcomes, over and over — diesel burning when the sun was already covering the load, batteries getting hammered until they die years early, and blackouts that catch everyone off guard because nobody was watching it coming.

## Slide 3
02 · SIGNIFICANCE & RATIONALE
Explainable Dispatch Decisions for Operator Confidence
An optimization problem, solved
Strip away the jargon and this is just: figure out what's coming, then pick the cheapest, cleanest mix that still keeps the lights on. LP and MILP solve that part fine — the research backs it up.
What actually surprised us: trust
If an operator watches diesel kick in with no idea why, they don't trust the system — they switch it to manual and go back to guessing. So explaining why isn't a nice-to-have bolted on at the end. It's load-bearing.
TATVA · UrjaSetu · HackOut'26
03 / 16
Notes: Strip away the jargon and this is just an optimization problem — figure out what's coming, then pick the cheapest, cleanest mix that still keeps the lights on. LP and MILP solve that part fine, the research backs that up. But here's what the papers kept saying that actually surprised us: the algorithm was never the hard part. Trust was. If an operator watches diesel kick in and has no idea why, they don't trust the system — they just switch it to manual and go back to guessing. So for us, explaining why isn't a nice-to-have bolted on at the end. It's load-bearing.

## Slide 4
03 · KEY CHALLENGES
Key Gaps Limiting Intelligent Microgrid Automation
Dispatch can't react to weather
Zero forecasting in the loop
Batteries dying early
Blackouts nobody predicted
Operators who don't trust a black box
Dashboards useless without signal
TATVA · UrjaSetu · HackOut'26
04 / 16
Notes: So we sat down and listed out what's actually broken: dispatch that can't react to weather, zero forecasting, batteries dying early, blackouts nobody predicted, operators who don't trust a black box, and — this one's easy to forget — a dashboard is useless if half your sites don't have decent signal.

## Slide 5
04 · PROJECT OBJECTIVES
Integrated Systems Bridging Infrastructure and Intelligent Control
1
Forecasting layer for generation and demand
2
Re-solving dispatch engine every fifteen to sixty minutes
3
Battery cost model accounts for long-term wear, not just today's bill
4
Blackout predictor looks ahead instead of reacting
5
An explanation on every decision attached at the source, not bolted on
Stretch goal: shiftable loads — nudging irrigation or cold storage into the hours when solar's cheap.
TATVA · UrjaSetu · HackOut'26
05 / 16
Notes: That turned into five things we're actually building: a forecasting layer for generation and demand, a dispatch engine that re-solves every fifteen to sixty minutes, a battery cost model that accounts for long-term wear — not just today's bill — a blackout predictor that looks ahead instead of reacting, and an explanation attached to every decision the system makes. We're also stretching into shiftable loads, so things like irrigation or cold storage can be nudged into the hours when solar's cheapest.

## Slide 6
05 · PROJECT SCOPE
Development Scope: Intelligent Dispatch and Decision Support
IN SCOPE
Simulated microgrid, optionally fed by a live BMS
Rule-based MVP graduating to a full LP / MILP solver
State-of-charge tracking
Blackout prediction
Dashboard + SMS alerts
What-if simulator
OUT OF SCOPE
Buying actual panels or hardware
Multi-year capacity planning
Trading carbon credits
Hooking multiple microgrids together
TATVA · UrjaSetu · HackOut'26
06 / 16
Notes: We're not pretending we can ship real hardware in a weekend, so here's where we drew the line. In scope: a simulated microgrid — optionally fed by a live battery management system — starting as a rule-based MVP and graduating to a full LP or MILP solver, plus SoC tracking, blackout prediction, a dashboard, SMS alerts, and a what-if simulator. Out of scope: buying actual panels, multi-year capacity planning, trading carbon credits, hooking multiple microgrids together. We're building the brain, not the body, and not the bank account.

## Slide 7
06 · TARGET STAKEHOLDERS
Integrated Solution for Key Stakeholder Requirements
Site operator
Needs a straight answer, fast — every fifteen minutes, without second-guessing it.
NGO field worker
Sometimes the answer has to arrive over SMS, because the phone doesn't hold a signal for a dashboard.
Community & funders
Fewer outages for the community; real numbers — diesel avoided, emissions avoided — for funders.
TATVA · UrjaSetu · HackOut'26
07 / 16
Notes: The person we're actually designing for is a site operator or an NGO field worker who needs a straight answer, fast — and sometimes that answer has to arrive over SMS because their phone doesn't hold a signal for a dashboard. Everyone downstream benefits too: the community gets fewer outages, and funders get real numbers — diesel avoided, emissions avoided — instead of a promise.

## Slide 8
07 · SYSTEM ARCHITECTURE
Five-Stage Architecture with a Continuous 15-Minute Decision Cycle
Weather, demand
& battery data
Optimization
engine
Solar · wind ·
battery · diesel
Blackout
validation
Dashboard
(cost · CO2 · reliability)
↺ re-runs every 15 minutes
TATVA · UrjaSetu · HackOut'26
08 / 16
Notes: Zoom out and the whole thing is one loop. Weather, demand, and battery data flow in. The optimization engine chews on that and decides the split across solar, wind, battery, and diesel, nudges any flexible loads, double-checks that nothing's about to go dark, and pushes the result to a dashboard tracking cost, CO2, and reliability. Then it does it again fifteen minutes later.

## Slide 9
08 · OPERATIONAL WORKFLOW
Six-Step Operational Workflow for Each Dispatch Cycle
1
Sense
battery & load, right now
2
Forecast
next one to six hours
3
Optimize
the dispatch plan
4
Dispatch
across four sources
5
Validate
blackout risk + explanation
6
Display
& log for sharper forecasts
Loops back to Sense — logging what actually happened against what was predicted, so the forecast gets sharper over time.
TATVA · UrjaSetu · HackOut'26
09 / 16
Notes: Broken into steps, that loop is: sense what the battery and load are doing right now, forecast the next one to six hours, optimize the dispatch plan, actually dispatch it across the four sources, validate — meaning check for blackout risk and write the explanation — display it, and loop, logging what actually happened against what we predicted so the forecast gets sharper over time.

## Slide 10
09 · OPTIMIZATION FRAMEWORK
Optimization Objectives and Operational Constraints
THE GOAL
Minimize:
Diesel cost + Emissions penalty + Battery wear cost
Re-solved every 15–60 minutes, fast enough in under a second (PuLP or scipy) to keep pace with the dispatch cycle.
CONSTRAINTS — NEVER BROKEN
Supply — must always meet demand
Battery floor — can't drop below its safety floor
Diesel cycling — can't switch on / off every 5 minutes
Fuel — can never go negative
Rule-based MVP first → graduated to a proper LP / MILP solver.
TATVA · UrjaSetu · HackOut'26
10 / 16
Notes: Under the hood, the engine's trying to minimize diesel cost, plus an emissions penalty, plus a battery wear cost — while never breaking four rules: supply has to meet demand, the battery can't drop below its safety floor, diesel can't be switched on and off every five minutes, and fuel can't go negative. We started rule-based just to get something working end to end fast, then moved up to a proper solver — PuLP or scipy, both fast enough to re-run in well under a second, which matters when you're re-deciding every fifteen minutes.

## Slide 11
10 · KEY INNOVATIONS
Key Innovations and Competitive Differentiation
A blackout predictor that looks ahead
Runs the simulation forward several cycles, so it catches a shortfall before it happens instead of after.
A degradation-aware cost function
Never saves two rupees of diesel today by wrecking a battery that costs a fortune to replace.
TATVA · UrjaSetu · HackOut'26
11 / 16
Notes: Two things we'd bet the demo on. One — a blackout predictor that runs the simulation forward several cycles, so it catches a shortfall before it happens instead of after. Two — a degradation-aware cost function, so the optimizer never saves you two rupees of diesel today by wrecking a battery that costs a fortune to replace.

## Slide 12
11 · AI-BASED FORECASTING
Integrated Weather and Historical Data for Six-Hour Forecasting
Solar
Irradiance × panel efficiency
Wind
Turbine's power curve
Demand
Same calendar date last year, blended with the last 7 days' trend
Renewables + Usable battery − Expected demand = Surplus / Deficit
That gap — surplus or deficit — is what actually drives the optimizer.
TATVA · UrjaSetu · HackOut'26
12 / 16
Notes: For generation, we work solar output off irradiance and panel efficiency, and wind off the turbine's power curve — nothing exotic. Demand's the more interesting one: we blend what happened on this same calendar date last year with the trend from the last seven days, weighted together into one forecast. Add up renewables plus usable battery, subtract what we expect demand to be, and that gap — surplus or deficit — is what actually drives the optimizer.

## Slide 13
12 · PREDICTIVE MAINTENANCE
Early Detection of Equipment Degradation
Performance ratio
What a unit is actually putting out, versus what it should be putting out — tracked continuously, panel by panel, turbine by turbine.
Careful about false alarms
One bad reading never triggers an alert on its own
The gap has to repeat, again and again
It has to look different from neighboring units
Otherwise a cloudy Tuesday looks like a broken panel — and that's not a system anyone keeps trusting for long.
Flagged only when the drop is persistent AND unit-specific — never on a single cloudy reading.
TATVA · UrjaSetu · HackOut'26
13 / 16
Notes: We also keep an eye on every individual panel and turbine using something called a performance ratio — what it's actually putting out versus what it should be putting out. And we were careful here: one bad reading doesn't trigger an alert. The gap has to show up again and again, and it has to look different from what the neighboring units are doing, before we flag it. Otherwise a cloudy Tuesday looks like a broken panel, and that's not a system anyone keeps trusting for long.

## Slide 14
13 · MONITORING & LOW-CONNECTIVITY INTERFACE
Dual-Mode Monitoring Through Dashboard and SMS
Live dashboard
Cost
CO2 avoided
Reliability
What-if simulator — type "three cloudy days in a row" and watch battery and diesel respond before it happens.
Historical replay — runs real past weather & load through the optimizer for a genuine before-and-after.
One plain SMS
"Diesel running, battery 15%, switching to solar around 2 PM."
Same information, same explanation — because a chunk of real users won't have a working smartphone on them.
TATVA · UrjaSetu · HackOut'26
14 / 16
Notes: On screen, an operator sees live cost, CO2 avoided, and reliability — plus two features we're genuinely proud of. A what-if simulator, so you can type "three cloudy days in a row" and watch battery and diesel respond before it's actually happened. And a historical replay mode that runs real past weather and load data through the optimizer and hands you a real before-and-after, not a guess. And because a chunk of our actual users won't have a working smartphone on them, the same information goes out as one plain SMS: "Diesel running, battery 15%, switching to solar around 2 PM."

## Slide 15
14 · TECHNOLOGY STACK
Technology Components for Reliable and Scalable Deployment
Core
Python — optimization & forecasting
Solver
PuLP or scipy
Weather
Open-Meteo or OpenWeatherMap
Alerts
Twilio (SMS layer)
Frontend
React + Recharts / D3
Backend
FastAPI or Flask + Postgres / SQLite
TATVA · UrjaSetu · HackOut'26
15 / 16
Notes: Nothing here is trying to be clever for its own sake. Python underneath for optimization and forecasting, PuLP or scipy for the solver, Open-Meteo or OpenWeatherMap for weather, Twilio for the SMS layer, React with Recharts or D3 on the front end, FastAPI or Flask with Postgres or SQLite holding it all together.

## Slide 16
15 · EXPECTED IMPACT & CONCLUSION
Expected Outcomes: Reduced Costs, Improved Battery Life, and Operator Confidence
Lower emissions
and proven, not promised — via replay mode
Lower fuel bills
diesel used only when it's actually needed
Batteries that last
the single most expensive asset on site
LP dispatch, weather forecasting, an SMS alert — people have built all of these before. What's ours is putting them together around the three things that quietly kill these projects: trust, connectivity, and whether the battery's still alive in year two.
That's Tatva. Thanks — happy to take questions.
TATVA · UrjaSetu · HackOut'26
16 / 16
Notes: So what does this actually buy someone? Less diesel, lower emissions, and — because of the replay mode — we can actually prove it instead of asking you to take our word for it. Lower fuel bills, and a battery that lasts as long as it's supposed to, which is usually the single most expensive thing on site. And an operator who keeps the system switched on, because it explains itself instead of just handing down verdicts. None of our individual pieces is a breakthrough on its own — LP dispatch, weather forecasting, an SMS alert, people have built all of these before. What we think is actually ours is putting them together around the three things that quietly kill these projects in the real world: trust, connectivity, and whether the battery's still alive in year two. That's Tatva. Thanks — happy to take questions.